## Slide 1: JIBEBE PROJECT 2023
<ELECTRICAL SUBSYSTEM>
TEAM :
EUNICE ORENGE
LABAN MWANGI
VICTOR MAINA
STEPHEN KINUTHIA

## Slide 2: OBJECTIVE
To design and fabricate the electric system for an electric tractor

## Slide 3: MAJOR COMPONENTS
A.C MOTOR 15kW, 3000 rpm
96V Slider ACIM Controller
96V 165Ah Battery
Charging system

## Slide 4: OPERATION
The first step to operate the electric tractor is to turn it on through the ignition.
This action activates the controller to allow power flow to the electric motor.
The tractor is still stationary and upon application of the either the travelling , reverse and working gears then pressing the accelerator , the tractor starts moving.
The travelling gear moves the tractor at high speed and low torque, favorable for movement in a smooth surface for example, a tarmac road.
The reverse gear moves the tractor in the opposite direction.
The working gear moves the tractor in low speed but high torque, favorable for tilling.
All these operations are managed by the controller which acts as the brain of the motor. It also inverts DC voltage from the battery to AC

## Slide 5: Power flow-chart
Source from Socket
Battery
Motor controller
Motor
Low Voltage DC Converter
Navigation systems
Lights and indicators

## Slide 6: testing

## Slide 7: testing
Battery testing
Motor testing

## Slide 8: A) BATTERY TESTING
Charging of the battery has not been tested since cable lugs are yet to be acquired.
The discharging of the battery is also yet to be determined, such that we know just how long it will take to discharge the battery.
There is a thought in the pipeline of incorporating a regenerative braking system that recharges the battery as the motor slows down, though a lot of research still needs to be done on the subject.
The output terminals of the battery were measured to be 106V DC.

## Slide 9: B) MOTOR TESTING
The motor testing was sub-divided into the following
1. Speed test
2. Braking test
3. AC output voltage of the controller
4. Navigation modes test

## Slide 10: 1.SpEED TEST
The speed of the motor was noticed to be relatively low after the installation/connection of the motor and this was first solved by interchanging the U and V phases which gave us an output speed of 4500rpm.
Later on, we interchanged the V and W phases and got a higher speed in relation to the previous speed. Though, we are yet to measure this speed. We are planning for the acquisition of the analogue tachometer from the Machines Lab to facilitate this measurement.
The speed test proved successful and we can bring it to a close after examining that there are no more possible ways to increase the output speed of the motor further

## Slide 11: 2. BRAKING TEST
  The testing of the braking system of the motor with the controls of the controller is still failing. We endeavor to re-check the connections and troubleshoot in subsequent tests.

## Slide 12: 3. THE OUTPUT OF THE CONTROLLER
  At first the output measured from the controller was 23V AC line to line. After interchanging the V and U phases in a bid to increase the output speed, the output of the controller was noticed to have increased to 26V AC line to line.
  A later interchanging of the phases to W and V causes an increase on the output voltage to a peak of 60V AC line to line and a constant of 50V AC when the throttle is accelerated to the maximum.
  The team is yet to investigate the theoretical knowledge or principle behind this behavior of the motor and controller, as all this information was arrived at after reading through the manual on the ACIM controller.

## Slide 13: 4. NaVIGATION MODES
There are three modes namely, forward , reverse and half speed.
The testing of all three was successful and though the interchanging of the phases caused a switch in the working of the reverse and forward modes, such that a command to move the motor in the forward direction moved it in reverse and vice-versa, the team was able to find a way around it and the test was brought to completion successfully.